## Slide 1: Design of Wireless Black Box for Cars
Prepared By:
MHD.Lutfe kassar
Supervised by:
D.Hassan ahmad
ENG.Mohamed othman
2026/11/3
Syrian Private University Faculty of Artificial Intelligence Engineering intelligent telecommunication Engineering

## Slide 2: Outline
Project Objective
Problem Statement & project Importance
Methodology
Reference studies
General theoretical Fundamentals
Reference LIST

## Slide 3: Project Objective
Design of Wireless Black Box for Cars

## Slide 4: Problem Statement & project Importance
Problem Statement:
Failure to detect dangerous situations that do not end in a collision
Failure to link visual evidence with sensor data
Relying on manual review of the recording
Project Importance:
Identifying near-miss incidents
Tracking vehicle location
Integrating multiple data sources

## Slide 5: Recent seminar
Creating a black box for cars based on the ESP32 microcontroller
Designed for monitor, record, and analyse important vehicle data during normal driving conditions by reading sensors (LM35,MPU6050,MQ3,Vibrator sensor…) and sent data to esp32
And store the data after processing it in simcard to see the parameter of sensor which installed on our project

## Slide 6: Methodology
Hardware Selection and Setup
Sensor Data Acquisition
Video Recording and Data Storage
Raspberry Pi Integration
Near-Crash Detection
System Testing and Evaluation

## Slide 7
Reference studies

## Slide 8
Paper reference | principle | Methodology
[1] Ultralytics, YOLO26 on Raspberry Pi Setup & Benchmarks | OLO detects objects in video frames and identifies their classes, such as cars and pedestrians, using bounding boxes and confidence scores. | OLO detects objects in video frames and identifies their classes, such as cars and pedestrians, using bounding boxes and confidence scores.communication
[2] Ultralytics, Multi-Object Tracking | Object tracking maintains object identities across consecutive video frames, allowing the system to monitor their movement and trajectories. | ByteTrack is used with YOLO detections to track vehicles and pedestrians. The resulting trajectories are analyzed to identify potentially dangerous interactions.
[3] Raspberry Pi Ltd., Raspberry Pi Documentation | The Raspberry Pi is a compact, single-board computer capable of running operating systems and software applications for image processing, sensor communication, and real-time data analysis. | The Raspberry Pi is used as the main processing unit for video analysis. It receives video from the camera, runs the object detection and tracking algorithms, and communicates with the ESP32 to combine visual information with sensor readings for potential near-miss detection.

## Slide 9: Theoretical Fundamental
Connecting ESP32 with Raspberry Pi for Near-Miss Incident Detection
The main idea of our Wireless Black Box for Cars project is to use the ESP32 to collect sensor data and the Raspberry Pi to analyze camera footage. By combining both sources of information, the system can identify potentially dangerous driving situations, known as Near-Miss Incidents.
I2C= Inter-Integrated Circuit

## Slide 10
Option 1: Wired Communication Using USB Serial
The ESP32 sends sensor readings to the Raspberry Pi through a USB cable
advantage | disadvantage
Easy to implement | Physical Cable Required
simple to debug | Cable Reliability
suitable for continuous sensor data transmission | The actual transmission rate depends on the USB interface, serial adapter, and communication settings

## Slide 11
Option2:Wireless Communication Using Wi-Fi
Communication method: Wi-Fi using TCP or MQTT.
The ESP32 transmits sensor readings wirelessly to the Raspberry Pi over a configured Wi-Fi connection.
advantage | disadvantage
flexible | Connection Instability
No direct communication cable is needed | Packet Loss and Delays
 | More Complex Configuration

## Slide 12
Models and Algorithms Used on the Raspberry Pi
Object Detection Models
YOLO (You Only Look Once)
Detects vehicles and pedestrians in individual video frames.
Provides bounding boxes, object classes, and confidence scores.
Lightweight versions can be deployed on Raspberry Pi.
Advantages: Fast inference and a good balance between speed and accuracy.
Limitations: Performance depends on lighting, camera quality, object size, and processing power.
SSD (Single Shot Detector)
Detects objects in a single forward pass.
Designed for efficient inference on resource-constrained devices.
Advantages: Lightweight and suitable for embedded computer vision.
Limitations: Accuracy can be lower than that of larger or better-optimized models in difficult scenes.
Faster R-CNN
Uses a two-stage detection process to propose regions and classify objects.
Advantages: Can provide strong detection accuracy.
Limitations: Generally more computationally demanding, making real-time deployment on a Raspberry Pi more challenging.

## Slide 13
Object Tracking Algorithms
Algorithm | Main characteristics | Limitations
SORT | Simple, fast tracking based mainly on motion and object association | Can switch object IDs during occlusion
DeepSORT | Combines motion with visual appearance features | Requires additional computation for appearance extraction
ByteTrack | Associates detections using high- and low-confidence detection results | Does not use appearance-based re-identification by default
OC-SORT | Uses observations to improve tracking under nonlinear motion and occlusion | Tracking can still fail when objects remain hidden for long periods
BoT-SORT | Combines motion, optional appearance features, and camera-motion compensation | More configuration and computation may be required

## Slide 14
Near-Miss Detection Algorithms
Rule-Based Detection
Combines predefined conditions, such as a vehicle entering the monitored path and a sudden deceleration event.
Easy to implement, explain, and test.
Time to Collision (TTC)
Estimates the remaining time before a potential collision if the interacting road users continue along their current trajectories and speeds.
Helps identify potentially critical interactions.
Post-Encroachment Time (PET)
Measures the time between one road user leaving a potential conflict area and another road user reaching that area.
Random Forest and LSTM
Machine-learning approaches that could classify events using sensor readings and temporal features.
LSTM: designed to learn patterns from sequences over time.

## Slide 15: Reference LIST
[1] Ultralytics, YOLO26 on Raspberry Pi Setup & Benchmarks
[2] Ultralytics, Multi-Object Tracking
[3] Raspberry Pi Ltd., Raspberry Pi Documentation